## Slide 1
Computer Networking
The Network Layer – Control Plane (part b)
Dr Mark Greenwood greenwm1@hope.ac.uk FML312
Drop In Hours
Thursday 12 – 2pm

## Slide 2
Reading
The course textbook:
Computer Networking: A Top-Down Approach
Seventh Edition
Kurose, J. K., and Ross, K. W.
ISBN 13: 978-1-292-15359-9
Useful additional reading:
Data and Computer Communications
Tenth Edition
Stallings, W.
ISBN 13: 978-9-332-58693-2

## Slide 3: Network Layer Control Plane
goals: understand principles behind network control plane
traditional routing algorithms
SDN controllers
Internet Control Message Protocol
network management
and their instantiation, implementation in the Internet:
OSPF, BGP, OpenFlow, ODL and ONOS controllers, ICMP, SNMP

## Slide 4
1 introduction
2 routing protocols
link state
distance vector
3 intra-AS routing in the Internet: OSPF
4 routing among the ISPs: BGP
5 The SDN control plane
6 ICMP: The Internet Control Message Protocol
7 Network management and SNMP
8 ASN.1 and BER
Outline

## Slide 5: Internet inter-AS routing: BGP
BGP (Border Gateway Protocol): the de facto inter-domain routing protocol
  “glue that holds the Internet together”
BGP provides each AS a means to:
  eBGP: obtain subnet reachability information from neighboring ASs
  iBGP: propagate reachability information to all AS-internal routers.
  determine “good” routes to other networks based on reachability information and policy
allows subnet to advertise its existence to rest of Internet: “I am here”

## Slide 6: eBGP, iBGP connections
eBGP connectivity
iBGP connectivity
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
1c
∂
∂
gateway routers run both eBGP and iBGP protocols

## Slide 7: BGP basics
when AS3 gateway router 3a advertises path AS3,X to AS2 gateway router 2c:
  AS3 promises to AS2 it will forward datagrams towards X
BGP session: two BGP routers (“peers”) exchange BGP messages over semi-permanent TCP connection:
  advertising paths to different destination network prefixes (BGP is a “path vector” protocol)
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS 2
AS 3
AS 1
X
BGP advertisement:
AS3, X

## Slide 8: Path attributes and BGP routes
advertised prefix includes BGP attributes
  prefix + attributes = “route”
two important attributes:
  AS-PATH: list of ASes through which prefix advertisement has passed
  NEXT-HOP: indicates specific internal-AS router to next-hop AS
Policy-based routing:
  gateway receiving route advertisement uses import policy to accept/decline path (e.g., never route through AS Y).
  AS policy also determines whether to advertise path to other other neighboring ASes

## Slide 9: BGP path advertisement
Based on AS2 policy, AS2 router 2c accepts path AS3,X, propagates (via iBGP) to all AS2 routers
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS2 router 2c receives path advertisement AS3,X (via eBGP) from AS3 router 3a
Based on AS2 policy, AS2 router 2a advertises (via eBGP) path AS2, AS3, X to AS1 router 1c

## Slide 10: BGP path advertisement
AS1 gateway router 1c learns path AS2,AS3,X from 2a
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
gateway router may learn about multiple paths to destination:
AS3,X
AS1 gateway router 1c learns path AS3,X from 3a
Based on policy, AS1 gateway router 1c chooses path AS3,X, and advertises path within AS1 via iBGP

## Slide 11: BGP messages
BGP messages exchanged between peers over TCP connection
BGP messages:
  OPEN: opens TCP connection to remote BGP peer and authenticates sending BGP peer
  UPDATE: advertises new path (or withdraws old)
  KEEPALIVE: keeps connection alive in absence of UPDATES; also ACKs OPEN request
  NOTIFICATION: reports errors in previous msg; also used to close connection

## Slide 12: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: “path to X goes through 1c”
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS2,AS3,X
AS3,X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
AS3,X
Q: how does router set forwarding table entry to distant prefix?
1
2
1
2
dest
interface
…
…
X
…
…
1
physical link
local link interfaces
at 1a, 1d

## Slide 13: BGP, OSPF, forwarding table entries
recall: 1a, 1b, 1c learn about dest X via iBGP from 1c: “path to X goes through 1c”
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
1d: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 1
Q: how does router set forwarding table entry to distant prefix?
dest
interface
…
…
X
…
…
2
1a: OSPF intra-domain routing: to get to 1c, forward over outgoing local interface 2
1
2

## Slide 14: BGP route selection
router may learn about more than one route to destination AS, selects route based on:
  local preference value attribute: policy decision
  shortest AS-PATH
  closest NEXT-HOP router: hot potato routing
  additional criteria

## Slide 15: Hot Potato Routing
2d learns (via iBGP) it can route to X via 2a or 2c
hot potato routing: choose local gateway that has least intra-domain cost (e.g., 2d chooses 2a, even though more AS hops to X): don’t worry about inter-domain cost!
1b
1d
1c
1a
2b
2d
2c
2a
3b
3d
3c
3a
AS2
AS3
AS1
X
AS3,X
AS1,AS3,X
OSPF link weights
201
152
112
263
Notes: ANIMATED SLIDE…
Click through and chat … emphasize that HOT POTATO is a selfish algorithm

## Slide 16: BGP: achieving policy via advertisements
A advertises path Aw to B and to C
B chooses not to advertise BAw to C:
  B gets no “revenue” for routing CBAw, since none of C, A, w are B’s customers
  C does not learn about CBAw path
C will route CAw (not using B) to get to w
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 17: BGP: achieving policy via advertisements
A,B,C are provider networks
X,W,Y are customer (of provider networks)
X is dual-homed: attached to two networks
policy to enforce: X does not want to route from B to C via X
  .. so X will not advertise to B a route to C
A
B
C
W
X
Y
legend:
customer
network:
provider
network
Suppose an ISP only wants to route traffic to/from its customer networks (does not want to carry transit traffic between other ISPs)

## Slide 18: Why different Intra-, Inter-AS routing ?
policy:
inter-AS: admin wants control over how its traffic routed, who routes through its net.
intra-AS: single admin, so no policy decisions needed
scale:
hierarchical routing saves table size, reduced update traffic
performance:
intra-AS: can focus on performance
inter-AS: policy may dominate over performance

## Slide 19
1 introduction
2 routing protocols
link state
distance vector
3 intra-AS routing in the Internet: OSPF
4 routing among the ISPs: BGP
5 The SDN control plane
6 ICMP: The Internet Control Message Protocol
7 Network management and SNMP
8 ASN.1 and BER
Outline

## Slide 20
Software defined networking (SDN)
Internet network layer: historically has been implemented via distributed, per-router approach
  monolithic router contains switching hardware, runs proprietary implementation of Internet standard protocols (IP, RIP, IS-IS, OSPF, BGP) in proprietary router OS (e.g., Cisco IOS)
  different “middleboxes” for different network layer functions: firewalls, load balancers, NAT boxes, ..
~2005: renewed interest in rethinking network control plane

## Slide 21
Recall: per-router control plane
Routing
Algorithm
Individual routing algorithm components in each and every router interact with each other in control plane to compute forwarding tables
data
plane
control
plane

## Slide 22
data
plane
control
plane
Recall: logically centralized control plane
A distinct (typically remote) controller interacts with local control agents (CAs) in routers to compute forwarding tables
Remote Controller
CA
CA
CA
CA
CA

## Slide 23
Software defined networking (SDN)
Why a logically centralized control plane?
easier network management: avoid router misconfigurations, greater flexibility of traffic flows
table-based forwarding (recall OpenFlow API) allows “programming” routers
  centralized “programming” easier: compute tables centrally and distribute
  distributed “programming: more difficult: compute tables as result of distributed algorithm (protocol) implemented in each and every router
open (non-proprietary) implementation of control plane

## Slide 24: Traffic engineering: difficult traditional routing
Q: what if network operator wants u-to-z traffic to flow along uvwz, x-to-z traffic to flow xwyz?
A: need to define link weights so traffic routing algorithm computes routes accordingly (or need a new routing algorithm)!
Link weights are only control “knobs”: wrong!
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x

## Slide 25: Traffic engineering: difficult
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can’t do it (or need a new routing algorithm)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x

## Slide 26: Traffic engineering: difficult
y
x
w
v
z
2
2
1
3
1
1
2
5
3
5
u
v
x
w
y
z
Q: what if w wants to route blue and red traffic differently?
A: can’t do it (with destination-based forwarding, and LS, DV routing)

## Slide 27
Software defined networking (SDN)
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized“ flow-based” forwarding (e.g., OpenFlow)
2. control, data plane separation
3. control plane functions external to data-plane switches
…
4. programmable control applications
routing
access control
load
balance
Notes: ANIMATED SLIDE
Overview of the 4 key characteristics of a SDN solution (revision)
Flow based forwarding - can be based on any number of header fields in transport, network or link layer headers! (OpenFlow uses 11 different headers – depends on entries in a switch’s flow table!) – traditional routing is IP dependent only
Separation of the data and control planes
Network control functions are absolutely external to the data plane
The network is programmable

## Slide 28
SDN perspective: data plane switches
Data plane switches
fast, simple, commodity switches implementing generalized data-plane forwarding in hardware
switch flow table computed, installed by controller
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable and what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 29
SDN perspective: SDN controller
SDN controller (network OS):
maintain network state information
interacts with network control applications “above” via northbound API
interacts with network switches “below” via southbound API
implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 30
SDN perspective: control applications
network-control apps:
“brains” of control: implement control functions using lower-level services, API provided by SND controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 31
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
Components of SDN controller
communication layer: communicate between SDN controller and controlled switches
Network-wide state management layer: state of networks links, switches, services: a distributed database
Interface layer to network control apps: abstractions API

## Slide 32: OpenFlow protocol
operates between controller, switch
TCP used to exchange messages
  optional encryption
three classes of OpenFlow messages:
  controller-to-switch
  asynchronous (switch to controller)
  symmetric (miscellaneous)
OpenFlow Controller

## Slide 33: OpenFlow: controller-to-switch messages
Key controller-to-switch messages
features: controller queries switch features, switch replies
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
read-state
send-packet: controller can send this packet out of specific switch port
OpenFlow Controller

## Slide 34: OpenFlow: switch-to-controller messages
Key switch-to-controller messages
packet-in: transfer packet (and its control) to controller. See packet-out message from controller
flow-removed: flow table entry deleted at switch (may be a response to a modify-state.
port status: inform controller of a change on a port.
Fortunately, network operators don’t “program” switches by creating/sending OpenFlow messages directly. Instead use higher-level abstraction at controller
OpenFlow Controller

## Slide 35
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra’s link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
S1, experiencing link failure using OpenFlow port status message to notify controller
1
SDN controller receives OpenFlow message, updates link status info
2
Dijkstra’s routing algorithm application has previously registered to be called when ever link status changes. It is called.
3
Dijkstra’s routing algorithm access network graph info, link state info in controller, computes new routes
4

## Slide 36
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
1
2
3
4
6
5
Dijkstra’s link-state
Routing
s1
s2
s3
s4
SDN: control/data plane interaction example
link state routing app interacts with flow-table-computation component in SDN controller, which computes new flow tables needed
5
Controller uses OpenFlow to install new tables in switches that need updating
6

## Slide 37
topology
manager
Basic Network Service Functions
REST API
OpenFlow 1.0
…
SNMP
OVSDB
forwarding
manager
switch
manager
host
manager
stats
manager
Network service apps
Service Abstraction Layer (SAL)
Access
Control
Traffic
Engineering
…
OpenDaylight Lithium (ODL) controller
ODL Lithium controller
Network-service apps may be contained within, or be external to SDN controller
Service Abstraction Layer: interconnects internal, external applications and services

## Slide 38
1 introduction
2 routing protocols
link state
distance vector
3 intra-AS routing in the Internet: OSPF
4 routing among the ISPs: BGP
5 The SDN control plane
6 ICMP: The Internet Control Message Protocol
7 Network management and SNMP
8 ASN.1 and BER
Outline